## Slide 1: CSCE 693 – Software Evolution Designing Video Game Hardware
Air Force Institute of Technology
Douglas D. Hodson, PhD
Bldg 640, Rm 311C
255-3636 x4719

## Slide 2: Part V – CPU Designs (Highlighted Comments)

## Slide 3: Table of Contents
Part V – CPU Designs
  Chapter 25: The ALU: Arithmetic Logic Unit
  Chapter 26: A Simple CPU
  Chapter 27: A Configurable Assembler
  Chapter 28: Racing Game With CPU
  Chapter 29: A 16-bit CPU
  Chapter 30: Framebuffer Graphics
  Chapter 31: Tilemap Rendering
  Chapter 32: Scanline Sprite Rendering
  Chapter 33: A Programmable Game System
  Chapter 34: A Demo Program

## Slide 4: Chapter 25 – The ALU
ALU : Arithmetic Logic Unit
  Takes two operands A and B, computes an operation (aluop) on them
  Combinational circuit, NOT sequential

## Slide 5: ALU Operations

## Slide 6: ALU Implementation

## Slide 7: Chapter 26 – A Simple CPU
FEMTO-8
  8-bit data inputs or operands
  8-bit address bus (can address 256 bytes of memory)
  Instructions are variable length
  No interrupt functionality
  A and B registers are 8-bits wide
  Y register used to store output from ALU
  Instruction pointer (IP) is 8-bits
CPU named “FEMTO” because it sounded cool

## Slide 8: MOS Technology 6507
6507: 8-bit microprocessor
Essentially a 6502, but
  Smaller, cheaper
  Address line A15-A13 and some other signals such as interrupt lines are not accessible
  Therefore can address 8KB of memory (2^13)
  Oriented at small-scale embedded systems, not general-purpose computers

## Slide 9: CPU Common Traits
A number of registers which store internal state
An instruction set which the CPU interprets in a fetch-decode-execute cycle
The ALU or arithmetic logic unit which computers math and logic functions
An address bus which identifies which external components (e.g., RAM, ROM) and which address to read or write
A data bus which contains the data to send of receive from external components
An instruction pointer (or program counter) that contains the address of the next instruction to execute
Fetch (an instruction from memory)
Decode (figure out what to do)
Execute (carry out instruction in a prescribed order)

## Slide 10: CPU Design: Competing Goals
Maximizing code density
  Define a rich set of instructions to reduce code size
Simplify decoding
  Design instructions to be easily decoded for execution
  FEMTO does this be defining some bits to have consistent meaning across multiple opcodes
    Bits 0-3 encode ALU operation
    Bits 4-5 encode destination register
    Bit 6 is set if the ALU input read from the data bus, otherwise it reads from register B
Modern CPUs decode instructions into micro-operations

## Slide 11: FEMTO-8 Instruction Encoding
Think operations and less about instructions
ALU operations ≠ CPU opcodes
This table present the encoding, examples are few, not all mnemonics!

## Slide 12: Assembly Mnemonic Syntax
Examples
  add A,B : adds the value in register B to register A, storing the result in A
  add A, #127: adds the constant value 127 to A (immediate mode)
  add A, [B]: fetches the data at address B, then adds it to A

## Slide 13: High Level Interface
Clock
Reset
Address to read from or write to
Data input
Data output
Write signal to indicate reading or writing

## Slide 14: CPU State Machine
SELECT: fetch the next opcode and increment the instruction pointer
DECODE: latch the opcode from the data bus and determine what’s next: write to memory, or proceed to the COMPUTE or READ_IP states
COMPUTE: latch the output of the ALU into a register, set carry and zero flags
READ_IP: used for taken conditional branches; reads a new IP from memory

## Slide 15: Important!
Nowhere in the FEMTO-8 source code will you find “instructions” listed
  You will find a state machine designed with certain features and capabilities
The job of the assembler is to map (encode) human readable instructions (mnemonics) to those capabilities

## Slide 16: Verilog Compiler Directives
A directive is used to control the compilation of a Verilog description
  (`) denotes a compiler directive
Examples
  `include : insert the entire contents of a source file into another file
  `define : define text macros
  `undef : remove text macro definitions
  `ifdef : checks to see if a macro has been defined to optional include source code
  `timescale : specified the time unit and precision of the modules that follow

## Slide 17: FEMTO-8 Macros
Interesting, but never used!

## Slide 18: State Machine: S_RESET
Reset sets the instruction pointer to $80 (128), then transitions to select
  $80 is halfway into our memory space of 256 bytes
  In theory this is where our ROM code goes, RAM would be from 0-$7F

## Slide 19: State Machine: S_SELECT
The output of IP is used to drive the address bus to read (write=0) opcode
Instruction pointer is incremented (need to correct if we branch)

## Slide 20: State Machine: S_DECODE
Decoding is the most complex logic in CPU
Using the current opcode available on the data bus (data_in) we determine what to do bases on the decoded bits
Notice that both swap and sta “instruction” opcodes can immediately be performed, and transition back to select
Verilog “casez” statement allows you to specify don’t care for certain bits – can match bit patterns
Two byte instructions

## Slide 21: State Machine: S_COMPUTE
Grabs ALU output and writes it to desired destination
Computes the carry flag
Computes the zero flag by NOR-ing all of the ALU output bits

## Slide 22: Chapter 27 – A Configurable Asm
A configurable assembler
  The mapping of assembly mnemonics to resulting binary is configurable and specified by a single JSON file

## Slide 23: 8 Bit Workshop IDE
Hardware and Software Code Being Executed
Assembly Code to Convert for Custom “FEMTO-8” CPU

## Slide 24: JSON-based Configuration File
The mapping of assembly mnemonics to resulting binary is configurable and specified by a single JSON file
  This provides a lot of flexibility to the custom CPU designer
Syntax
Data is in name/value pairs - separated by commas
Curly braces hold objects
Square brackets hold arrays

## Slide 25: JSON Format: Rules
Configuration file format has a number of rules
  Each rule has a format that matches a line of assembly code, and a bit pattern that is emitted when matched
  Each rule effectively defines one of more assembly mnemonics
“rules” are defined by an array of objects, where each line defines a “transformation” from mnemonic to bits
(This table defines all mnemonics)

## Slide 26: Example: swapab
Interchanges A and B registers
  “swapab” is the human readable mnemonic, “10000001” is the resulting bit pattern needed and read by CPU
“fmt” attribute defines the pattern to be matched
  If matched, the “bits” attribute defines machine code to emit

## Slide 27: JSON Format: Variables
Can specify different types of variables
  const4 can store 4-bit values
  imm8 can store 8-bit values
To include variable in a rule, prefix the variable’s name with a tilde (~)
  The instruction encoding process uses the variable’s value (which might be an explicitly defined token)
  The value is determined by the index of the token array (e.g., 0 for first variable, 1 for second)

## Slide 28: Example: sta
Stores register A into specified memory address
  “sta” is the human readable mnemonic, “1001nnnn” is the resulting bit pattern needed and read by CPU
“fmt” attribute defines the pattern to be matched
  Looking for a variable that will map to 4-bits
  “bits” is specified to take 0th item (the value of variable) and concatenate with “1001” (it’s the “nnnn” part of the opcode)
Rule
Variable

## Slide 29: JSON Format: Tokens
A variable’s value can be defined by tokens
Tokens map to value (register example)
  a: 00
  b: 01
  ip: 10
  none: 11
reg: register, unop: operation, binop: binary operation, const4: constant, imm8: immediate value

## Slide 30: Example: mov
Example
  Variable encodes a, b, ip, or none into 2-bits
  Using this rule, for this instruction “mov a, [b],” results in “11” + “00” + “1011”
Notice that “mov” instruction is not explicitly shown in Opcode list (these are examples!)
mov a, [b]
Rule
Variable

## Slide 31: JSON Format: Branching
Branches are taken based upon CPU status (carry & zero flags)
Branches are specified by an immediate value (address), 8-bits wide – hence 256 bytes can be addressed
The immediate value is determined by the assembler
lower 4-bits of opcode (tttt)

## Slide 32: Assembler Directives
.arch <arch> : load the file <arch>.json and configures the assembler
.org <address> : the start address of the ROM, as seen by the CPU
.len <length> : the length of the ROM file output by the assembler
  Use this to match the output from assembler to length of the ROM array
.width <value> : the size in bits of a machine word (default is 8)
.define <label> <value> : define a label with a given numeric value
.data $aa, $bb, ... : include raw data in the output
.string .... : converts a string to machine words, and includes it
.align <value> : align the current IP to a multiple of <value>

## Slide 33: FEMTO-8 Complete Example
Starting address for output is $80 (128)
Loop label set to address $83
Branch on carry moves the instruction pointer back to $83 until carry not set

## Slide 34: Chapter 28 – Racing Game w/CPU
Implement a racing game using FEMTO-8 CPU and two sprites
High level perspective
  Memory map

## Slide 35: Hardware

## Slide 36
High Level Architecture
Architecture consists of a CPU, video sync generator, bitmap for a car and two sprite renderers
CPU can access RAM, some inputs and ROM
Sprite renderers read bitmap at different points of time, and supply output in terms of a gfx bit

## Slide 37: Multiplex CPU Data Bus

## Slide 38: Sprite Rendering (Reading Bitmap)

## Slide 39: Collision Detection
frame_collision is set if player car collides with enemy car or track
Bit available to CPU at address $42 (i.e., IN_FLAGS) in memory map

## Slide 40: Synthesis Issues
Some assignments within CPU state machine need to be registered
  Sprite renderer module needed this as discovered in previous homework
  Tested changes within browser simulator first to see any obvious behavioral changes (nothing found)
Separated “ALU” module from CPU and modified slightly
  Other ALU examples found “on web” always registered output result
  Since it’s now registered, no need to do so within CPU reg [8:0] Y -> wire [8:0] Y

## Slide 41: Initial Synthesis Result

## Slide 42: Doing Lots of Nothing
Keep CPU busy in endless loop while debugging hardware
Static display – CPU does nothing
$6B

## Slide 43: Initializing Registers (i.e., ROM)
ref: Recommended HDL Coding Styles, Quartus II 9.1 Handbook, Volume 1
(We will use $readmemh – reads memory file in hex format)

## Slide 44: $readmemb / $readmemh
Reads a memory file
  “b” means data values specified in binary
  “h” means data values specified in hexadecimal
“mem” files are just text files with data

## Slide 45: Warning! Accessing RAM Issue
Different aspects of the circuit accessing (reading and/or write) to the same “RAM” registers
Warning in Book!

## Slide 46: Removing Direct RAM Access
Both sprites render correctly at the position specified, if hardcoded (as opposed to reading RAM)
Quick “fix” – check to see if sprites render correctly

## Slide 47: Dual Ported RAM (With a Single Clock)

## Slide 48: What is it?
Dual ported RAM is memory that allows any combination of independent read or write operations in the same clock cycle
In our game, the CPU updates car positions (writes) while the sprite renderers possibly read that value – at the same time (or the same clock cycle)
  Using dual ported RAM resolves that issue

## Slide 49
Example: 64-bit x 8-bit Synchronous
Single clock
RAM data flows in through two ports (data_a, data_b)
RAM data flows out through two ports (q_a, q_b)
Independent write enable signals (we_a, we_b)
Dual-port RAM or DPRAM is a type of RAM that allow multiple reads and writes simultaneously at different addresses

## Slide 50
Racing Game RAM: 16 x 8-bit Synchronous
Single clock
RAM data flows in through two ports (data_a, data_b)
RAM data flows out through two ports (q_a, q_b)
Independent write enable signals (we_a, we_b)

## Slide 51: Issue of Concern
Dual Ported RAM Partial Fix, We Really Need Something Different
Need simultaneous access to it
Want to read values from several locations all at once
If I can’t I need to sequence through reading values, looking for “matches” to trigger sprite renderer – in other words, I need another state machine to trigger the sprite renderers state machine

## Slide 52: Separate Registers
Write player and enemy position information to their own registers directly accessible by decision logic
  This is basically what was done for custom graphics chips – the chips had their own registers
Add these new registers to memory map

## Slide 53: New Memory Mapping

## Slide 54: Nearly 100% Working!

## Slide 55: Issues of Concern
VGA is a 640x480 resolution screen
  Therefore, player and enemy position is specified by 10 bits…. but the CPU can only read 8!

## Slide 56: Resolution
Upgrade CPU to 10-bits
  Or upgrade aspects of it, like reading and writing 10-bits of memory with internal 10-bit registers, but maybe instructions still stored as 8
  Chapter 29 touches on some of this (CP1600 which powered the original Intellivision had 16-bit data and address buses, and instructions that were only 10-bits wide)
Limit size of playfield to 256x256
  Turn off display outside of that range
  Then trigger the loading of player and enemy cars bitmaps outside of that range

## Slide 57: Software (I Need a Way to Assemble Code and Easily Initialize Registers)

## Slide 58: Assembler Source Code
Entire assembler is written in TypeScript, in a single file (assembler.ts: 374 lines)
  Appears to be written as a module
Developer supplied a test script (testasm.js: 116 lines) to check assembler

## Slide 59: ASM.EXE Example
Validation
(Website)

## Slide 60: Racing Car Game Program
Using assembler, generate opcodes and reformat hex values into a “mem” file to be loaded by Quartus to initialize register array

## Slide 61: EOF

## Slide 62: Parts
After Complete